## Slide 1: METHODS IN PARASITOLOGY
KIMAIGA H.O
MBChB (University of Nairobi)

## Slide 2: Laboratory Diagnosis of Parasitic Infections
Purpose –
  Confirmation of clinical suspicion
  Identification of unsuspected infection
Methods same as used in Bacteriology & Virology but significance of different methods varies.
Isolation least important, morphological identification very important.
Serology relatively less important

## Slide 3: Morphological identification
Examination of faeces –
  Gross
  Microscopy
    Saline mount
    Iodine Mount
    Thick smears – not commonly used
    Permanent stained smears
      Iron hematoxylene
      Whearley’s trichrome stain
  Concentration methods
    Floatation techniques
    Sedimentation techniques

## Slide 4: Morphological identification
Examination of Blood
  Thin Smear
  Thick smear
  Wet mount for microfilaria
  Stains used

## Slide 5: KATO-Katz technique for helminth eggs
Materials:
Kato-set
(Template with hole, screen, nylon or plastic, plastic spatula)
Newspaper or glazed tile
Microscope slides
Cellophane as cover slip, soaked in Glycerol-malachite green solution
Fresh stool
Gloves

## Slide 6
Prepare the layer
Glazed tile or newspaper
Place the template with hole in the centre of a microscope slide
Use gloves!

## Slide 7
Place a small amount of faecal material on the newspaper or the glazed tile.
Press the screen on top so that some of the faeces filters through and scrape with the flat spatula across the upper surface to collect the filtered faeces.
Add the collected faeces in the hole of the template so that it is completely filled.

## Slide 8
Remove the template carefully so that the cylinder of faeces is left on the slide.
Cover the faecal material with the pre-soaked cellophane strip.
Invert the microscope slide and firmly press the faecal sample against the cellophane strip on a smooth hard surface such as a tile

## Slide 9
The material will be spread evenly.
Carefully remove the slide by gently sliding it sideways to avoid separating the cellophane strip. Place the slide with the cellophane upwards.
The smear should be examined in a systematic manner and the eggs of each species reported.
Later multiply by the appropriate number (seeinlet-information of the Kato-set) to give the number of the eggs per gram faeces.

## Slide 10: Adhesive tape method for the detection of pinworm eggs
Clear adhesive tape
Microscope slides
Gloves
(Xylene or Butyl acetate)

## Slide 11
Use gloves! (pinworm eggs are infectious!)
Prepare the tape
Take sample on peri-anal skin in the morning
Stick tape on microscope slide
4-6 negative tapes are needed to rule out a pinworm infection!

## Slide 12
Picture under microscope:
  Tape without Butyl acetate /Xylene produces many air bubbles!
Place a drop of Xylene on the edge of the tape to remove air bubbles
Picture under mikroscope:
  Without air bubbles

## Slide 13: Cultivation of parasites
Culture methods –
  Amoeba
  Leishmania & Trypanosoma
  Malarial parasite
Animal inoculation – Not practical
Xenodiagnosis – Vectors infected experimentally
Immunological diagnosis

## Slide 14: Immunological diagnosis
Serology – All tests available
  IHA
  ELISA
  CIEP
  IF
  CFT
More useful in
  Amoebiasis
  Leishmaniasis
  Malaria
  Toxoplasmosis
  Trichinosis
  Filariasis
  Echinococcosis
Skin Tests – Specificity low, cross reactions common
  Casoni’s test
  Leishmanin test

## Slide 15: Need for Serodiagnosis
1. Unattainable parasitological diagnosis
  Special specimens & Tests,
    Trichinosis- muscle biopsy
    Toxoplasmosis- lymph node, placenta
  Long prepatent period
    Filariasis
  No method available, e.g., gnathostomiasis
  Micros. exam of excreta tedious, time-consuming, impractical
  Negative in light infection, e.g., strongyloidiasis, opisthorchiasis
2. Cost-effective in epidemiological survey
  Labour
  Time

## Slide 16: Drawbacks of serodiagnosis
1. Specificity and sensitivity not 100%
2. Depending on host's immune response- e.g., ocular parasitosis
3. Sophisticated and expensive equipment
4. Well-trained personnel

## Slide 17: Antibody Assay
1. Skin or intradermal test
  Easiest to perform
  Type I & IV hypersensitivity
  Type I-> helminthiases
  Type IV->protozoan infections

## Slide 19
2. Complement fixation test (CF)
3. Precipitin methods -Double diffusion in agar (DD) -Counterimmunoelectrophoresis (CIEP) -Immunoelectrophoresis (IEP) -Nephelometry

## Slide 20
CIEP for cysticercosis

## Slide 21
4. Agglutination methods
  Direct agglutination (DA)
  Bentonite flocculation (BF)
  Latex agglutination (LA)
  Indirect hemagglutination (IHA)

## Slide 22
5. Labelled reagent methods
  Label with fluorescein dye
  Immunofluorescence (IF)- FITC, rhodamine
P. falciparum
Toxoplasma

## Slide 23
ABTS-substrate
OPD-substrate
  Label with enzyme
    Enzyme immunoassay- ELISA

## Slide 24
-Electroimmunotransfer blot (EITB)

## Slide 25: Antigen assays
Merits:
Appear earlier than antibody
Amount directly varies with degree of infection
Not persist
Commercial kit
Intestinal amoebiasis, giardiasis, cryptosporidiosis, etc.

## Slide 26: Method:
Use monoclonal or polyclonal antibodies in CIEP, ELISA
DNA detection by PCR

## Slide 27
ICT (immunochromatographic assay)

## Slide 29: Validation of immunoassays
Most important = Predictive value (PV)
PV - A measure of how accurately a test can predict the presence or absence of disease when applied under special circumstance
PV depends on Sensitivity, Specificity and Prevalence
Sensitivity = % diseased population whose tests are POSITIVE
Specificity = % nondiseased pop whose test are NEGATIVE
Prevalence = % diseased pop in total population tested

## Slide 30: Definition
PV for positivity (%) = % of positive-test population who really get disease
PV for negativity (%) = % of negative-test population who really don't have disease
PV(+) decreases when prevalence of disease decreases

## Slide 31
280 Serum specimens
  80 cases with Ascaris eggs in stool
    40 cases = positive
  200 normal volunteers with negative stool examination
    10 cases = positive
Example- ELISA for ascariasis

## Slide 32
Category n Test results
+ -
Disease 80 40 (TP) 40 (FN)
No disease 200 10 (FP) 190 (TN)
Sensitivity = 40/80 x 100 = 50%
Specificity = 190/200 x 100 = 95%
Prevalence = 80/(80+200) x 100 = 28.6%

## Slide 33
PV(+) = TP/(TP+FP) x 100
= 40/(40+10) x 100 = 80%
Category n Test results
+ -
Disease 80 40 (TP) 40 (FN)
No disease 200 10 (FP) 190 (TN)

## Slide 34
Category n Test results
+ -
Disease 80 40 (TP) 40 (FN)
No disease 200 10 (FP) 190 (TN)
PV(-) = TN/(TN+FN) x 100
= 190/(190+40) x 100 = 82.6%
Under the condition that prevalence of the disease = 28.6%

## Slide 35
Interpretation
Test applied to 300 villagers where prevalence of ascariasis = 25.6%
  90 are positive, 210 are negative
  PV(+) = 80% means that from 90 above, only (90 x 0.8) = 72 cases really have disease
  PV(-) = 82.6% means that from 210 above, only (210 x 0.826)= 173 cases do not have disease

## Slide 36
What happen if tested with 1000 villagers with the prevalence of ascariasis about 5% ?
1000 villagers
(0.05 x 1000) = 50 cases have ascariasis; test sens = 50%, so only 25 cases are positive (TP=25, FN=25)
(.95 x 1000)=950 cases do not have infection; test spec.=95%, so only (.95 x 950)= 860 cases are negative (TN=860, FP=90)
PV(+) = 25/(25+90) x 100 = 21.7% (decreased from 80%)
PV(-) = 860/(860+25) x 100 = 99.4% (increased from 82.6%)

## Slide 37: Nematodes
Capillaria philippinensis
Enterobius vermicularis
NEMATODE AND CESTODE EGGS FOUND IN STOOL SPECIMENS OF HUMANS

## Slide 38
Trichuris trichiura
Ascaris lumbricoides fertile

## Slide 39
Ascaris lumbricoides infertile
Hookworm

## Slide 40
Trichostrongylus spp.

## Slide 41: Cestodes
Taenia spp.
Hymenolepis nana

## Slide 42
Hymenolepis diminuta
Diphyllobothrium latum

## Slide 43
Dipylidium caninum